## Slide 1: Digital Image Processing
Computer Vision

## Slide 2: Digital Image Acquisition Process
reflection or absorption (e.g., X-rays) of energy
e.g., lens to focus light on image plane

## Slide 3: Energy Sources

## Slide 4: Electromagnetic Spectrum
examples:
visible band: digital camera
microwaves: radar
X-rays: computed tomography (CT)
radio band: magnetic resonance imaging (MRI)
gamma rays: positron emission tomography (PET)
Crab Nebula in multiple wavelengths
source

## Slide 5: Lidar vs Cameras for Self-Driving Cars
Lidar:
similar to radar, but using lasers
very accurate
camera:
human-like perception
cost-effective

## Slide 6: Examples for other Energy Sources
ultrasound
electron beams (electron microscopy)

## Slide 7: Image Formation

## Slide 8: Bare-Sensor Imaging
digital sensor
all scene points contribute to all sensor pixels:
image plane

## Slide 9: Pinhole Camera
camera: barrier with pinhole (aperture)
each scene contributes to one pixel only
camera obscura

## Slide 10: Pinhole Camera Model
focal length
scaled object projection
object distance
3D world coordinates to 2D image coordinates :
losing depth …

## Slide 11: Lens Camera
ideal pinhole is infinitesimally small: larger diameter/aperture makes image blurrier (but also allows more light to pass through: higher intensity of image pixels)
 use optical lens
lens camera can be described with pinhole camera model, if:
only central rays are considered
lens camera is in focus (focus distance of lens camera equal to focus length of pinhole camera)

## Slide 12: Digital Image Sensors

## Slide 13: Photons to Electrons
to be digitized
largely replaced chemical and analog imaging
single sensor: photodiode
sensor strips: motion perpendicular to strip for imaging in other direction, used in CT
sensor arrays: used in digital cameras (in focal plane, outputs proportional to integral of light received at each sensor)

## Slide 14: Most Popular Sensors: CCD and CMOS
larger light-sensitive areas, lower noise level
 used in high end video cameras
lower power consumption, typically smaller
 used in most consumer product cameras
active pixel sensor
no individual silicon cells, but microlenses on top of each pixel to focus light on sensitive areas
pixel

## Slide 15
camera shutter opens
photodiodes: photons to electrons, store in potential well
camera shutter closes
read-out of potential wells, conversion to analog signals
conversion to digital signals (intensity levels)

## Slide 16: Pixels & Intensity

## Slide 17: Digitizing: Sampling & Quantization
digitizing the coordinate values: pixels
digitizing the amplitude values: discrete intensity levels

## Slide 18: Discrete Intensity Levels
image data: 2D grid (matrix) of pixels with different intensity values
intensity resolution:
common to use one byte (28) to express possible intensity values (8-bit image)
 0 = black, 255 = white
storage requirement for, e.g., 8-bit image (grayscale): ~1 MB
(3 for RGB color images)
source

## Slide 19: Image as Two-Dimensional Function
image can be seen as function : intensity at position
digital image: discrete (sampled and quantized) version of this function

## Slide 20: Contrast
range of intensity levels:
maximum measurable intensity determined by saturation
minimum detectable intensity determined by noise
contrast: difference in intensity between highest and lowest intensity levels in an image
intensity histograms:

## Slide 21: Intensity Transformations
e.g., image enhancement through contrast manipulation
contrast stretching (expanding range of intensity levels):
thresholding (differentiation of foreground and background regions):
lighten or darken image simply by adding or subtracting a fixed value from the pixel intensities

## Slide 22: Power-Law Transformations
simultaneous spreading and compression of intensity levels
e.g., gamma correction:

## Slide 23: Histogram Equalization
automatic contrast stretching
global transformation function: based on intensity distribution of entire image
local histogram equalization by restricting transformation to pixel neighborhoods
after histogram equalization:
number of pixels in bin
number of pixels
maximum intensity level

## Slide 24: Spatial Resolution
pixels per unit distance: e.g., pixels per inch (ppi)
 determines print size of digital image with given pixel count
do not confuse digital image resolution with screen resolution
e.g., iPhone 16 Pro Max: pixels, 6.9 inches diagonal  460 ppi
also, do not confuse with dots per inch (dpi): property of the printer
same resolutions
image size: number of pixels

## Slide 25: Example from Astronomy
Vera C. Rubin Observatory
first light expected in 2025
largest digital camera ever made: 3.2-gigapixel CCD

## Slide 26: Color

## Slide 27: Colors in the Human Eye
retina: image sensor of human eye
two kinds of light receptors on surface of retina: rods (monochromatic vision) and cones (color-sensitve cells)
three types of cones: red, green, blue
 combinations of red, green, and blue create perceived colors

## Slide 28: Primary Colors
standardization:
use of specific wavelengths for three primary colors red, green, and blue
 can reproduce (almost) all visible colors by mixing with different intensities
for printing:
primary colors of pigments each absorb one primary color of light

## Slide 29: RGB Color Model
color model for monitors and cameras
(other color models: CMYK, HSV, ...)
RGB 24-bit color cube
( bits)
color pixels:
3 intensity “channels”

## Slide 30: Color Sensing
single image sensor with one of three color filters in front of each pixel
estimation of missing color values for each pixel by interpolation from neighboring pixels
 full-color image

## Slide 31: Image Compression

## Slide 32: Need for Compression
crucial for storage and transmission
example HD TV:
image resolutions of bits
digital video as sequence of full-color still images (frames) with 30 frames per second
 2-hours video 1.34 TB

## Slide 33: Compression & Decompression
reduce spatial and temporal redundancy: exploit correlations between pixels
remove “irrelevant visual” information  irreversible process (lossy compression)
minimizing coding redundancy: shortest code words assigned to most frequent intensity values (variable-length code)
JPEG, GIF, PNG, …

## Slide 34: Example: Block Transform Coding
drop or coarsely quantize least important transform coefficients
decorrelate pixels of each sub-image by means of discrete 2D transform
e.g., discrete cosine transform (DCT) or wavelet transform
DCT kind of approximated principal component analysis (PCA)
encode quantized coefficients (e.g., Huffman coding)
DCT basis functions:
often

## Slide 35: Neighborhood Operators

## Slide 36
Single-Pixel/
intensity transformations

## Slide 37: Spatial Filtering
linear shift-invariant operators:
replace each pixel’s intensity by weighted sum of its neighborhood
weights determined by a kernel (aka mask or filter)
same kernel shifted to all pixels
for example, filter of size :

## Slide 38: Example: Box Filter
:
results in local (moving) averages
 blurring (smoothing) effect:
We set the filter coefficients manually here.
Later, we will use a CNN for this.
without normalization resulting image would be saturated
the larger the filter size, the heavier the blurring effect
filters of even size possible as well, but odd-sized ones easier to deal with
the larger the kernel, the heavier the smoothing effect

## Slide 39: Definition: Correlation vs Convolution
using our example with filter of size
correlation:
convolution:
convolution of a kernel with a discrete unit impulse yields copy of the kernel at location of the impulse (and impulse filter yields image copy)
corresponding correlation instead yields rotated version of the kernel (or rotated image)
corresponds to flip of filter

## Slide 40
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 0 |  |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 0 | -1 |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 0 | -1 | -2 | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 0 | -1 | -2 | 
 | -1 |  |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 0 | -1 | -2 | 
 | -1 | 1 | 1 | 
 | -1 | 2 | 1 | 
…
step 1:
step 2:
step 3:
step 4:
result:
correlation

## Slide 41
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 1 |  |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 1 | 2 |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 1 | 2 | -1 | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 1 | 2 | -1 | 
 | 1 |  |  | 
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
=
 | 1 | 2 | -1 | 
 | 1 | 1 | -1 | 
 | -2 | -1 | 0 | 
…
step 1:
step 2:
step 3:
step 4:
result:
convolution
flip

## Slide 42: Padding
On last slides, we did not let the filter extend beyond image borders.
 boundary effects: resulting image smaller than original
zero-padding to avoid this:
1 | 2 | -1
1 | 1 | -1
-2 | -1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
=
0 | 0 | 0 | 0 | 0
0 | 1 | 2 | -1 | 0
0 | 1 | 1 | -1 | 0
0 | -2 | -1 | 0 | 0
0 | 0 | 0 | 0 | 0
zero-padding darkens the image edges
other padding options:
set to constant border value
repeat edge values
…
can also be more zero rows/columns (depending on image and filter size)

## Slide 43: Other Linear Smoothing Filters
when constructing filters (not only smoothing filters, but in general), look for separable ones:
allow to compute 2D convolution as two subsequent 1D convolutions (horizontal and vertical)
for image of size and kernel of size :
operations for non-separable filter
operations for separable filter
 significant speedup possible
bilinear filter (tent):
Gaussian filter:
corresponding horizontal 1D kernels
sampled from 2D Gaussian function
(larger requires larger kernel)

## Slide 44: Median Filter
same kind of neighborhood-shifting over image
but instead of weighted average, use median of intensity values in pixel neighborhood (no filter coefficients)  non-linear filter
very effective to reduce outliers, e.g., shot or salt-and-pepper noise
original:
average-filtered ():
median-filtered ():

## Slide 45: Sharpening Filters
goal of smoothing filters:
removal of small details, noise reduction
goal of sharpening filters:
highlight intensity transitions (e.g., edges)
averaging analogous to integration
 sharpening by differentiation
playground

## Slide 46: First- and Second-Order Derivatives
partial derivatives in discrete form:
1D visualization:

## Slide 47: Approximated Image Gradient
alternative formulation (1D):
 1D derivative filter:
Sobel filters:
1 | 0 | -1
-1 | 0 | 1
1
2
1
smoothing
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
horizontal
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
vertical
1 | 2 | 1
-1
0
1
smoothing
convolved with an image:
(convolution kernels)
 gradient with smoothing
construct separable filters:

## Slide 48: Magnitude of Image Gradient
magnitude/amplitude of gradient:
magnitude is isotropic
for sharpening:
add this to original

## Slide 49: Different Gradient Filters
the larger ones add smoothing components
(Sobel: convolution with bilinear filter)

## Slide 50: Alternative: Laplacian
isotropic for rotations in increments of 90°
to yield isotropic results for rotations in increments of 45°:
again, add to (or rather subtract from when using this filter definition here) original to get sharpened image:
0 | 1 | 0
1 | -4 | 1
0 | 1 | 0
filter mask:
1 | 1 | 1
1 | -8 | 1
1 | 1 | 1
scaled to visualize negative values
zero-crossings  edges

## Slide 51: Another Alternative: Unsharp Masking
use of smoothing filters for sharpening
smoothing of original image (e.g.,by Gaussian filter)
subtract the blurred image from the original  unsharp mask (similar to second-order derivative)
add unsharp mask to original image  sharpened image
similar to second-order derivative

## Slide 53: Fourier Transform

## Slide 54
Fourier analysis allows to determine frequency characteristics of images or filters
image
frequency content

## Slide 55: Frequency Representation of Spatial Function
response of a spatial function (filter) to a sinusoid with frequency :
Fourier transform: tabulation of magnitude and phase response at each frequency
Fourier transform pair:
frequency domain
complex: needs to capture both amplitude and phase
angular frequency
notation: sometimes or

## Slide 56: Fourier Transform Formulas
for continuous signals:
Discrete Fourier Transform (DFT):
inverse Fourier transforms:
unique only in range

## Slide 57: 2D Fourier Transforms
e.g., digital images ( and as width and height in pixels)

## Slide 58: Filtering in Frequency Domain
low-pass filtering:
high-pass filtering:
 smoothing
 sharpening (if added to original)
magnitude

## Slide 59: Gaussian Filters in Frequency Domain
low-pass filter
high-pass filter

## Slide 60: Importance of Phase

## Slide 61: Convolution Theorem
spatial domain:
frequency domain:

## Slide 62: Convolution via Fourier Transform
convolution of images with large spatial filters can be computationally heavy
 more efficient in frequency domain, thanks to Fast Fourier Transform (enabling convolution times independent of filter size)
also, construction of filters often easier in frequency domain

## Slide 63: Example: Gaussian Smoothing

## Slide 64: Fourier Transform Pair: Box and sinc Function
inverse scaling (valid for any function):
wider in spatial domain  more compressed in frequency domain (and vice versa)
(e.g., narrow and broad Gaussian)
in spatial domain, interpolations between samples (e.g., intensity values at image pixels) formed by infinite sum of sinc functions (approximated with bilinear or bicubic interpolations)
real part of for visualization

## Slide 65
sharpening filters / high-pass filters
smoothing filters / low-pass filters
some smoothing
approximated sinc
approximated Gaussian

## Slide 66: Band-Reject and Band-Pass Filters
periodic noise can be effectively removed with band-reject filters in frequency domain
notch reject filter

## Slide 67: Deconvolution
application of convolution theorem: inverse filtering in frequency domain to get rid of degradation effect
(image restoration)
more complicated in practice:
degradation function usually not known completely  need for estimation
usually also additive noise on top  need for noise suppression during deconvolution (Wiener filter)
example: motion blur
point spread function

## Slide 68: Aliasing

## Slide 69: Sampling
remember: digital images sample intensity values at each pixel

## Slide 70: Undersampling
aliasing: higher-frequency signal disguised as one of lower frequency

## Slide 71: Moiré Effect
aliasing in digital images often manifests itself as ringing patterns
temporal aliasing can be observed as wagon-wheel effect (apparent backward motion) in image sequences (video): frame rate too low with respect to speed of wheel rotation

## Slide 72: Sampling Theorem
continuous signal can be recovered from its samples, if sampling rate exceeds Nyquist frequency:
 no aliasing
Fourier transform of band-limited function:
digital images: no aliasing if ,
with number of pixels
(second dimension accordingly)

## Slide 73: Anti-Aliasing in Digital Images
no problem if signal is oversampled: number of pixels higher than twice the maximum frequency of image (for both width and height)
if not oversampled: smooth the signal
 removing some details (i.e., high frequencies,) that cause aliasing
optical anti-aliasing filter in digital cameras (on top of image sensor): cut out frequencies above Nyquist frequency

## Slide 74: Example: Shrinking
smoothing crucial before subsampling (shrinking) to avoid aliasing: decreases Nyquist frequency of image (to counter less pixels)
average of black and white

## Slide 75: Image Pyramids

## Slide 76: Gaussian Image Pyramid
sequence of sub-sampled images (one use case: features at different scales)
apply smoothing before each down-sample step (to avoid aliasing), typically by convolution with binomial kernel (converging to Gaussian)

## Slide 77: Laplacian Image Pyramid
retain only residuals at different levels (allows later upsampling, starting from highest-level image)
difference of Gaussians approximate Laplacian:

## Slide 78: Wavelets
discrete wavelet transform:
mapping of discrete function (e.g., a digital image) to sequence of coefficients (of a set of basis functions)
performing sub-band coding (decomposition of an image into set of band-limited components) combined with progressive down-sampling (similar to residual pyramid)
original ():
four sub-bands
low-low (further split in next level)
low-high (horizontal edges)
high-low (vertical edges)
high-high (mixed derivatives)
four sub-bands
four sub-bands
smallest image approximation
(only low-pass filters)